CMW+ 3.0.1 Installation Cover Letter (cmw435c.doc) v1.0

The purpose of this document is to describe how to install and configure
your system so that it will match the configuration submitted for
evaluation at ITSEC security level F-B1/E3.


1. Hardware Platform

There are three different hardware platforms submitted for evaluation:

   * Unisys SMP 5400
   * Elonex PC590/1
   * Elonex PC571/1


2. Software

   * SCO CMW+ 3.0.1
   * SLS cmw002a
   * SLS cmw003a
   * SLS cmw435c
   * SLS cmw489b

For the Unisys SMP 5400, you will also need:

   * SCO MPX for CMW+
   * SCO AHS 3.4 Multiprocessing Drivers
   * Adaptec 7800 Manager Set v1.20
   * Cogent SCO UNIX ODT 3.0 Driver for EM727, EM932, EM935 and EM845

For the Elonex PC590/1, you will also need:

   * SCO MPX for CMW+
   * SCO AHS 3.4 Multiprocessing Drivers
   * Adaptec 7800 Manager Set v1.20

For the Elonex PC571/1, you will also need:

   * Symbios Logic SDMS 3.0 BTLDPCI-3.04.00


3. Verifying Software Authenticity

Your CMW+ 3.0.1 software and manuals will have been delivered to you
individually shrink-wrapped. You should check when you receive them that
the shrink-wrap is intact, and you should check for the presence of the
Certificate of Licence and Authenticity, with the SCO hologram affixed.

If either the software or manuals have been tampered with or you do not
receive all of the media and manuals that you expected, then you should
contact the supplier of the software before continuing the installation.

To verify the authenticity of the additional software diskettes, you should
contact your SCO support representative, who will provide you with a list
of diskette names and checksums which you can use to check the authenticity
of your diskette copies.

The additional third-party driver diskette images are available for ftp
from the following locations:

ftp://ftp.sco.com/TLS/tls607adp.dd.Z   (Adaptec 7800 Manager 1.20)
ftp://ftp.sco.com/TLS/tls607cgn.dd.Z   (Cogent network card drivers)
ftp://ftp.sco.com/TLS/tls607smb.dd.Z   (Symbios Logic BTLD 3.0.4)

The procedure for creating diskettes from these images is described in the
accompanying document on the ftp site:

ftp://ftp.sco.com/TLS/tls607.ltr


4. Installation Procedure

Before beginning installation, you should ensure that you have noted the
documentation errata specified and referred to in section 12 of this
document. You are advised to mark up your documentation set where changes
are necessary.

Note on Re-linking the Kernel:

You will be asked if you wish to re-link the kernel several times during
the installation procedure. It is not strictly necessary to re-link the
kernel at each step, but you must ensure that, after the question has been
asked, the kernel is re-linked at least once before the system is next
rebooted. You can re-link the kernel manually by entering the following
commands:

    cd /etc/conf/cf.d
    ./link_unix

You should reply "yes" to the prompts asking whether to make this kernel
boot by default, and whether to rebuild the kernel environment.

Installation Instructions:

Follow the installation procedure as described in chapter 2 of the SCO CMW+
Installation and Upgrade Guide, with the following additions:

If you are installing from a SCSI tape device, first make sure that it is
configured as SCSI device ID 2. If you are installing from a CD-ROM, first
make sure that it is configured as SCSI device ID 5.

If your system's BIOS supports power management, ensure that it is disabled
before beginning installation.

At step 4, type "link". At the prompt asking for the package name, enter
"alad" for the Unisys SMP 5400 and Elonex PC590/1, or enter "bscam" for the
Elonex PC571/1. When prompted, insert the appropriate BTLD diskette
(Adaptec for "alad", Symbios Logic for "bscam"). Continue with step 5 in
chapter 2.

At step 8, follow the on-screen prompts. At the "Installation Setup"
screen, choose "Overwrite" for your installation type. At the "Software
Setup" screen, deselect the NFS package from "Optional Components".

At step 15, you will be asked for mail subsystem configuration information.
Follow the on-screen prompts.

At step 17, for the Elonex PC575/1, you may see the message "Cannot create
/usr/tmp/buffer" displayed; this message is harmless and should be ignored.

At step 23, invoke "custom" to begin installation of the supplementary
diskettes (the operation of custom is described in Appendix H of the
Installation Guide).

By selecting "Install", "A New Product", install each of the following
diskettes in turn:

   * SCO CMW+ Maintenance Supplement 1:
     these diskettes are included in the CMW+ box.
   * MPX for CMW+ disk (if necessary):
     when prompted, enter your MPX serial number and activation key. It is
     not necessary to install the Open Desktop version of MPX on this
     system.
   * SCO AHS 3.4 Multiprocessing Drivers (if necessary):
     you should select only the "APIC" driver.

At this point, the kernel should be rebuilt - you should answer "yes" to
the prompts asking whether the new kernel should boot by default, and
whether to rebuild the kernel environment. You then should reboot the
system to use the new kernel by ending "custom", and typing the command
"reboot" - remove any diskette that may still be in the drive. At the
single user mode prompt, enter the "root" user name and password to
re-enter system maintenance mode.

At this point, you should set the system time, and reset the root password,
in order to avoid a problem with the password change time previously being
set incorrectly (if you do not do this, you may experience problems when
you first enter multi-user mode). First you will need to remove the last
successful password change time from root's protected password entry - edit
the file /tcb/files/auth/r/root, and remove the text beginning "u_succhg#"
and finishing at the first following ":". For example, if the relevant line
in the file had been:

    :u_minchg#0:u_succhg#833382840:u_unsucchg#833381773:u_pickpw:\

you should change it to:

    :u_minchg#0:u_unsucchg#833381773:u_pickpw:\

To set the system time and reset the password, enter the following
commands, and follow the on-screen prompts:

    /etc/asktime
    /tcb/lib/passwd

Invoke custom again, and using "Add a New Product" install the following
diskettes, in this order:

   * SCO CMW+ File System SLS (cmw002a)
   * SCO CMW+ PPP SLS (cmw003a)
   * SCO CMW+ ITSEC Evaluation SLS (cmw435c)
   * SCO CMW+ Year 2000 SLS (cmw489b)

At this stage, for the Unisys SMP 5400, you should also install the network
card driver from the Cogent EISA Ethernet Drivers diskette. Choose the
"Packages" option, rather than "Entire Product", and select the "emC"
(EM935) driver.

Continue with step 24 in chapter 2 of the Installation Guide.

At step 25, for the Elonex PC590/1 and PC571/1, select the "nat" (NE2000)
network driver.

At step 31, run "mkdev graphics" directly. For the Unisys SMP 5400 only,
select the Cirrus Logic GD5424 controller. For the Elonex PC590/1 and
PC571/1, select the Tseng Labs ET4000 controller.

You should ensure that the kernel has been re-linked, and then reboot the
system, before attempting to enter multi-user mode (step 32).


5. Additional Configuration

On-line Manual Pages

As shipped, the configuration file for the man(C) command does not display
manual pages in the documented order. To correct this, make the following
changes by editing the file /etc/default/man:

Change the line beginning MODE= to read:

MODE=ALL

Change the line beginning ORDER= to read:

ORDER=C:c:1:S:s:2:3:CP:CT:5:M:m:1m:7:F:f:HW:hw:DOS:TC:tc:ADM:adm:
ADMN:admn:X:1X:x:XS:3X:3x:SFF:sff:4:STR:str:MP:mp:UCB:LOCAL

(note that the above should be entered as a single line, although it is
shown here as two lines.)


Printer Paper Size

To correctly support the A4 paper size for labelling when using the hpjet3
interface script, you should make the following change to the file
/usr/spool/lp/admins/lp/interfaces/printer, where printer is the name of
the printer you have previously configured:

After each occurrence of the character string

\033E

insert the character string

\033&l26A

(note the letter 'l', not the digit '1', above)

This character string should occur three times in the file. Note that if
you are using the USA standard paper size, you should not make this change.


Protecting telnet and ftp Passwords

In order to disallow clear-text passwords with both telnet and ftp, you
should ensure that the entries for both telnetd and ftpd in the file
/etc/inetd.conf do not give the argument "-c". The shipped configuration
file includes the -c flag for telnetd, so you should edit /etc/inetd.conf
to remove it from that line.


Disabling the rlogin Command

To avoid the danger of possible snooping of passwords from network packets,
you should disable the rlogin service. This is done by inserting a '#'
(comment) character in the file /etc/inetd.conf, at the start of the line
beginning "m6login".


Other Network Services

No other changes should be made to the supplied /etc/inetd.conf file; in
particular, you should not uncomment the lines which would enable UDP
services.

Note that, as specified in Chapter 4 of Administering Network Services in
the SCO CMW+ System Administrator's Guide, the BIND name service,
named(ADMN), is not supported and should not be enabled.


Changing Home Directory for Pseudo-Users

As shipped, the home directory settings for the pseudo-users dos and asg
can expose the system to a security vulnerability. To correct this,
carefully edit the file /etc/passwd (modifying this file incorrectly can
result in locking out the system) to make the following changes:

On the line beginning "dos:", delete the 3 characters "tmp" from before the
end of the line:

        dos:*:16:11:DOS device:/:

On the line beginning "asg:", delete the 7 characters "usr/tmp" from before
the end of the line:

        asg:*:8:8:Assignable devices:/:


Initialising Audit Parameters

You should initialise the audit parameter files before enabling auditing
for the first time. This is done by executing the following command as
root:

        mkaud -p -s

You should also set the default action for when auditing fills available
disk space to shut down the system. This parameter may be changed using the
Security Officer interface menu Audit, Maintenance, Modify Audit
Parameters.


Removing Account Locked Notification

To avoid the risk of an intruder using the account locked notification in
order to verify a guessed password despite the maximum number of failed
logins already having been attempted, you should edit the file
/usr/lib/X11/errors/XAuthMgr/AuthErrors. Locate each of the following
paragraphs of text:

    The account is locked due to an excessive number of unsuccessful
    login attempts. Please contact your site security officer.

    The terminal is locked due to an excessive number of unsuccessful
    login attempts. Please contact your site security officer.

    The host is locked due to an excessive number of unsuccessful
    login attempts. Please contact your site security officer.

Each of these paragraphs in turn should be replaced with the single line:

    Login incorrect - please try again


Additional sendmail Configuration

Locate the following text in the file /usr/lib/sendmail.cf:

    # default UID (bin)
    Ou2
    # default GID (mail)
    Og7

This text should be changed to:

    # default UID (nouser)
    Ou28
    # default GID (nouser)
    Og28


Disabling mscreen

mscreen is not functional on CMW+, but it is installed with the
set-user-id attribute.  To remove the risk of this being used to
compromise system security, disable it by executing the following
command as root:

        chmod 0 /usr/bin/mscreen


Information Labels

Note that your system, when installed as described in this cover
letter, will have display of information labels disabled by default.
This is the configuration of the system as evaluated.

If you should choose to enable information labels (see p224 of the
Trusted Facility Manual), the enforcement of MAC labels will still
be in effect, but the window manager will display both the MAC label
and the information label.  

As display of information labels was not included in the evaluation,
and due to the potential confusion between MAC labels and information
labels, it is recommended that you not enable this.


Avoiding Use of Unsecured Utilities

Chapter 13 of the SCO CMW+ Release Notes lists a number of system utilities
which have not been modified specifically for CMW+. Commands marked 3 will
in general work on CMW+, but do not support use with CMW+ specific
extensions, such as sensitivity labels, file privileges and multi-level
directories. Commands marked 5 will in general not work reliably on CMW+.
To ensure that the integrity of your system is not compromised, you should
avoid use of both these categories of commands.


Security-unaware Commands (3)

S51K, S52K, XENIX

You should inform sysadmin-authorised users to not select these file system
types when creating new file systems (note that S52K is not included in
this release in any case), as they do not support extended security
attributes.

backup, restore

These commands do not pose any risk to system integrity when run by
unprivileged users; however, you should ensure that privileged users are
aware that these commands should not be used for routine system backups, as
the security attributes of files will not be preserved.

btldinstall

This command is not accessible to unprivileged users. It could be used by
privileged users, but note that it will make changes to the kernel which
are likely to render your system incompatible with the configuration
submitted for evaluation.

clean_screen

This command fails to operate on CMW+.

cleantmp

Although this command will work on CMW+, note that it is not
multilevel-directory aware, and so will only remove temporary files at the
sensitivity level at which it is started. The invocation of cleantmp from
the root crontab has been disabled in CMW+.

ecc, eccd

These utilities are not supported on CMW+. Note that they are disabled by
default - you should not enable them with mkdev eccd.

frec

This utility does not recognise extended format file system images, and
therefore will fail to extract files from a volcopy(ADM) image made from
your system (only extended format file systems should have been on your
system, see S51K, etc. above). The only way to recover files from the
volcopy image is to copy the entire image back to a mountable file system.

fsname

This utility does not recognise extended format file system images, and
thus will fail to display or set volume names on your system, which will
have only extended format file systems (see S51K, etc. above).

install

This command may be used as documented, but note that it is not capable of
setting extended security attributes on files.

layers

Use of the layers(C) command is not supported on CMW+. Note that the
command will fail unless layers has previously been configured. You should
not configure layers (mkdev layers) on your system.

listen

This utility (/usr/net/nls/listen) fails to operate on CMW+.

logger

This utility (/etc/logger) is not supported on CMW+. It is only executable
by privileged users, and should not be invoked.

mscreen

mscreen is not supported on CMW+. Since serial terminals are not included
in the evaluated configuration, it is not operative in any case.

passmgmt

This NIS utility is not included in CMW+.

pt_chmod

Note that SLS cmw435c includes a fixed version of pt_chmod, so that it can
be used without risk of compromising system integrity.

sysadmin

This utility is not included in CMW+.

uucp

The UUCP suite of programs is not included in CMW+.

win

This command is a front-end to the dos DOS-Merge command, and is subject to
the same restrictions on use (see section 6 below).

finger, fingerd

The finger(C) command is only supported on the local machine; incoming
finger requests are rejected, as the fingerd daemon is not configured by
default on CMW+.

gettable, htable, whois

These commands are inoperative on CMW+, as no nicname server is provided.

logger, syslogd

Use of /usr/bin/logger and /etc/syslogd is not supported in the evaluated
configuration. Note that syslogd(ADMN) is not started by default, and
therefore logger(TC) is ineffective.

mkhosts

mkhosts(ADMN) has not been enhanced to check for authorisations or raise
privileges, so it must be run by a privileged user such as root in order to
run successfully.

named, rarpd, rexecd, routed, talkd, timed, uucpd

These network daemons are not supported on CMW+ and should not be enabled
in /etc/inetd.conf.

ntp

ntp utilities are not included in CMW+.

rmail

As UUCP is not supported on CMW+, the rmail(ADM) command is not functional.

ruptime

As rwhod is not included in CMW+, this command is not functional.

rwho, rwhod

These utilities are not included in CMW+.

slattach

SLIP is not supported on CMW+, so the slattach(ADMN) command will fail.

talk

As talkd is not started by default in CMW+, this command is not functional.


Unsupported Commands (5)

ale, ap, authckrc, authsh, chg_audit, cps, execbprg, fixmog, goodpw,
passwdupd, pwconv, pwunconv, relax, report.expire, report.login,
report.term, rmuser, sddate, smmck, tcbck, ttys_update, ttyupd, unretire,
useshell, zeroexit

These OpenServer utilities are not present on CMW+.

rmnttry, rmount, rumount

These utilities can only be run by root. As RFS remote file sharing is not
supported on CMW+, these utilities are obsolete and should not be used.

sulogin

This utility cannot be run by unprivileged users. It is not used on CMW+,
and as noted on the manual page, sulogin(ADM), it should not be directly
invoked in any case.

pppd

Note that SLS cmw003a includes an enhanced version of pppd, which operates
correctly on CMW+.


6. Additional Notes on Creating Users

All users of the system should each have a new account created for them.
When creating a user account, do not reuse any of the account names or user
id numbers that are already assigned by the system (the System
Administrator interface will show a warning if you attempt to do this).

Normally, users will not be allocated more than one account each and no user
will have have more than one account per workstation.  If, for operational
reasons, it is necessary for a user to have more than one account, the
system administrator will brief that user as to the correct usage of that
account in accordance with their organisation's security policy.

When creating a user account, do not assign that user to any of the groups
which are already defined on the system as shipped, except the group
"group". You may create new groups to include your users in as you wish.

When creating a new group, do not use any of the group id numbers that are
already in use (the System Administrator interface will show a warning if
you attempt to do this).

When unlocking a newly-created account, you should set that user's password
parameters using the Security Officer interface. You should select either
that the user will be assigned system-generated passwords, or that the user
may choose their own password. If you allow the user to choose their own
password, you should also select the "Perform triviality checks" option.

When modifying user account parameters, you should not disable the "Maximum
number of unsuccessful logins" field in the login controls.

Note that, as access to the DOS Merge facility is not part of the evaluated
configuration, you should not assign the "dos" command authorisation to
untrusted users.

Finally, note that when a user account is retired, that user may still have
batch jobs enabled (see the manual pages for the commands at and cron).
These batch jobs should be deleted manually.


7. Configuring Remote Hosts

Enable network communications between your systems by setting up the
security parameters for each pair of communicating hosts, as documented in
the MaxSix Administrators Guide, chapter 2. Do not include any unlabelled
hosts (as described in chapter 3) on your network.

Note that, in order to unlock the automatically configured host entries for
"localhost" and the entry for the name you chose for your system, you must
first have selected the corresponding entry or entries in the remote hosts
database in the Network Security Officer Role program, and chosen "Add" to
update the host's entries in the terminal control database.

For each user that you wish to be able to execute the rcmd utility, you
should create a .rhosts file (see the rhosts(SFF) manual page) in that
user's home directory on each remote system, including entries specifying
only that user's user name, together with the name of each of the systems
from which they will be executing the rcmd utility. You should not make use
of system-wide settings in the /etc/hosts.equiv file unless you also ensure
that each of the systems you have enabled communications between will have
identical sets of user names and ids.


8. Modifying the Standard Encodings File

In certain cases, you may find it necessary to modify your Encodings file
to change the classifications and compartments which are considered valid
on your system. Modifying the Encodings file after initial system boot is
not recommended. If it is considered necessary to make such a modification,
it should be done as soon as possible to avoid the potential loss of
information.

Changing the Encodings file is an involved procedure. If you do not
carefully follow the instructions listed below, you may leave the system in
a state where it can not boot. If you need more information on the basic
concepts and structure of the Encodings file, you should refer to the
document entitled Defense Intelligence Agency Compartmented Mode
Workstation Labeling: Encodings Format. This document is available from the
Defense Intelligence Agency to qualified recipients.


Precautions

A major consideration when preparing to replace the Encodings file is files
that currently exist on the system. The only sensitivity labels that will
be the same before and after the change are syslo and syshi. You should
note that the actual meaning of syslo and syshi may change with the
Encodings file. If files exist on the system at any other sensitivity
levels, they may be inaccessible after the change. You should reset the
sensitivity label of these files to syslo or syshi before attempting to
change the Encodings file.

Similar consideration should be given to any multilevel directories that
exist on the system. Note that the only child directories that will be
accessible after an Encodings file change are those that map to syslo and
syshi. You should carefully check all multilevel directories and move any
files in such child directories to a safe location. You should also remove
the child directories as a matter of general cleanup.

If your system is running on a network with other trusted systems,
additional consideration must be given to the affect on the network. The
MaxSix databases on the target machine must be modified to correctly
reflect the new Encodings file. Additionally, the mappings file
/tcb/files/M6MAPPINGS residing on each additional trusted system that
networks with your system will need to be modified to account for the new
Encodings file.

A final consideration is the Audit subsystem. You should note that any
previous audit trails will be unusable after a modification to the
Encodings file. Additionally, previously created report selection files may
be unusable as well.


Installing an Encodings File

To install the new Encodings file:

Step 1: From the Audit Menu of the ISSO Role Program on the Trusted Path,
disable auditing.

Step 2: Bring the system down to single-user mode by selecting Single User
Mode from the Trusted Path Menu. Move the existing Encodings database and
file to a safe place.

% cd /etc/policy/macilb

% mv Encodings.db Encodings.db.safe

% mv Encodings Encodings.safe

Note that the ASCII version of the Encodings file may not exist on your
system.

Step 3: Make a safe copy of the configuration file:

% cp config config.safe

Step 4: Load the new ASCII Encodings file in /etc/policy/macilb/Encodings.

Step 5: Edit /etc/policy/macilb/config to reflect the new Encodings file.

The first line after the comments should be modified to match the
classifications, compartments, and markings in the Encodings file. The
third number should be set to the highest "value" + 1 for Classifications.
The fourth number should be set to the highest "compartment" + 1, and the
fifth number should be set to the highest "marking" + 1.

Take, for example, this segment of an Encodings file:

CLASSIFICATIONS:

name=UNCLASSIFIED;  sname=U;  value=1;
name=CONFIDENTIAL;  sname=C;  value=2;
name=SECRET;        sname=S;  value=4;
name=TOP SECRET;    sname=TS; value=5;

INFORMATION LABELS:

WORDS:

name=REL;                   prefix;
name=LIMDIS;     sname=LD;  suffix;
name=ORCON;      sname=OC;  prefix;
name=eyes only;  sname=eo;  suffix;

name=nato;                  minclass=C;  compartments=1;
name=alfa;                  minclass=C;  compartments=2;
name=siop;                  minclass=C;  compartments=3;
name=ultra;      sname=ul;  minclass=C;  compartments=5;
name=sac;                   minclass=S;  compartments=7;
name=trident;    sname=tr;  minclass=S;  compartments=8;

name=UK;                                 markings=0;  prefix=REL;
name=Canada;     sname=can;              markings=1;  prefix=REL;
name=proj1;                 minclass=C;  markings=14; suffix=LIMDIS;
name=proj2;                 minclass=C;  markings=6;  suffix=LIMDIS;
name=comp1;      sname=c1;  minclass=C;  markings=9;  prefix=ORCON;
name=comp2;      sname=c2;  minclass=C;  markings=15; prefix=ORCON;
name=ceo;                                markings=8;  suffix=EO;
name=vp;                                 markings=10; suffix=EO;

The highest classification "value" shown is 5, therefore the number used
would be 6. The highest "compartment" listed is 8, so the number used would
be 9. The highest numbered "marking" is 15, which would make the number
used 16. The resultant config file would appear as:

/tcb/files/MACILBDBASE 64 20 6 9 16 3 2 1 1 2 1

Note that it is not necessary that the value be the highest number
incremented only by 1. Values can be the highest number incremented by any
integer.

Step 6: Convert the ASCII Encodings file to binary format using the
labelcomp(1M) command:

% /tcb/bin/labelcomp -o Encodings.db Encodings

Step 7: Move the Mandatory Access Control policy tag database aside and
create a new one:

% cd /tcb/files

% mv MACILBDBASE MACILBDBASE.old

% mkdb MACILBDBASE 1024 50

Step 8: Reboot the system, and re-enter single-user mode.

Step 9: Use the initauthdb(1M) command to re-initialise the System Default
database and the u_clearance field in the protected password entry for
root:

% /tcb/lib/initauthdb

Step 10: Modify the various security databases to replace references to
invalid labels.

These files include:

/etc/auth/system/devassign
/etc/auth/system/default
/tcb/files/auth/*/*
/usr/lib/X11/mand_appear

Instructions for modifying the mand_appear file can be found in the chapter
"Trusted Window System", section "Configuring Mandatory Appearance
Parameters".

Note that the designations syslo and syshi may be used.

Step 11: In order for the changes to take affect, you must shutdown and
reboot the system:

% sync
% reboot

Step 12: Run setfiles(1M) to ensure the proper set of permissions and
sensitivity labels on all files:

% /tcb/bin/setfiles

Step 13: Re-initialise the audit parameter files:

% /tcb/bin/mkaud -a


Updating the MaxSix Databases

When the preceding instructions have been successfully completed, the
Network Security Officer (NSO) will need to modify various MaxSix databases
to reflect the new Encodings file. It is suggested that these steps be done
while in single-user mode.

The MaxSix interface control database, /tcb/files/M6IDB should be examined
to see if any of the interface entries specifically list a sensitivity
label. In each entry, the four fields of interest are min_sl, max_sl,
def_sl, and def_ilb. These fields should be modified to reflect valid
sensitivity and information labels with regard to the new Encodings file.
Note that syslo and syshi are valid labels. Refer to the M6IDB(4) manual
page for more information on this file.

All entries of the MaxSix remote host database, /tcb/files/M6RHDB should be
checked to see if the fields min_sl, max_sl, and def_sl refer to valid
sensitivity labels with regard to the new Encodings file. Note that syslo
and syshi are valid labels. Refer to the M6RHDB(4) manual page for more
information on this file.

The MaxSix translation rules, /tcb/files/M6MAPPINGS will also need to be
modified to correctly translate to and from the sensitivity labels as
determined by the new Encodings file. Note that once the M6MAPPINGS file
has been modified, the m6parser(1M) program should be run to compile it
into its binary form, /tcb/files/M6BINMAP. Note that changes to the
M6MAPPINGS file may need to be made to the other trusted systems on the
network if they wish to properly communicate with your system. Please see
the chapter entitled "Advanced Administration" in the MaxSix
Administrator's Guide for details.

When all the MaxSix databases have been successfully modified to reflect
the new Encodings file, the system should be rebooted. Even if none of the
MaxSix databases needs to be modified, you must run m6parser(1M) if the
/etc/policy/macilb/config file has been altered.


9. Use of the root Account

When you have completed the installation process, and created privileged
accounts with access to the ISSO, SysAdmin and NSOI role programs, you will
no longer need to use the root account in normal operation. You should
note, however, that the root account may still be necessary in order to log
in to the system if security databases become corrupted. For this reason,
you should change the root password to an obscure setting (a system
generated password of at least 10 characters is recommended), and keep a
note of the password in a secure place, so that it can be used if your
system becomes otherwise inaccessible (this could occur due to power
failure or hardware failure).


10. Maintaining System Security

Following the initial configuration of your system, you should continue to
run periodic checks on the access controls for remote hosts - it is
possible for users to add their own .rhosts files which may allow access
from untrusted hosts. To check for the presence of these files, you should
run the following command from an account with allowdacread and
allowmacread privileges:

    find / -name .rhosts -print

You should check the contents of these files to verify that they do not
violate your site's security policy.

Note that the m6dbinteg(1M) command will also perform automatic checks on
many aspects of remote hosts configuration, including .rhosts files - you
may wish to set up a cron job to automatically execute this command on a
regular basis and mail the output to a responsible person.


11. Advice on Setting or Changing Passwords of Other Users

In this section, "administrator" refers to the ISSO or another user with
the "password" command authorisation:

The administrator is responsible for generating and assigning the initial
password for each user.  In addition, a user may forget their password or
the administrator may determine that a user's password may have been
compromised.  To be able to correct these problems, the administrator may
also change the password of any user by generating a new one.  The
administrator does not have to know the user's existing password in order
to do this.  Positive identification of the user should be sought by the
administrator when a forgotten password must be replaced.

When a user's password has been set or changed by the administrator,
the user is identified by the system as having an "expired password"
which will require the user to change the password by the usual procedure
before receiving authorisation to access the system.

If the user is not physically present when their password is set or
changed by the administrator, the new password must be communicated to
the user by a secure means.  Conveyance of passwords through third
parties or through unprotected electronic mail messages should be
avoided.  The administrator should seek confirmation from the user
of receipt of the password within a reasonable time.


12. Documentation Notes

Open Desktop/Open Server Documentation

The SCO CMW+ package includes some printed and on-line documentation that
refers to SCO Open Desktop or Open Server. Whilst the majority of that
documentation is applicable to SCO CMW+, you should be aware that in some
cases information is superseded by SCO CMW+ specific documentation. Where
topics are present in both, the CMW+ document always takes precedence.

Online Manual Pages

The ftp manual page security addendum, ftp(c), indicates that ACLs are
preserved; this is incorrect. The correct behaviour is documented in the
Security Features User's Guide, page 175.

Documentation Errata

The SCO CMW+ Release Notes list additional documentation errata on pages
78, 102 and 155-156.

User Documentation

Errata for the Security Features User's Guide is presented in Appendix A.
You may wish to provide that appendix separately to your users.

Administrator Documentation

Release Notes

Pages 30-32: Disregard references to the on-line document Features and
Limitations; this document is not provided with, and is not applicable to,
SCO CMW+.

Installation and Upgrade Guide

Page 26, step 25: Disregard the text from "You should also configure …" to
the end of this step.

Page 27, step 34: Replace the text "XIsso" with "XSysAdmin". Note that the
relevant page of the Trusted Facility Manual is page 47.

Page 41: Replace the text "return to step 13 ... (page 24)" with "return to
step 18 ... (page 25)".

Page 58: Replace the text "step 14" with "step 32".

Page 89: Add the following step:

9. Exit sysadmsh by pressing <Escape> to return to the main menu, selecting
Quit, and then confirming your selection.

System Administrator's Guide

Page 53: Replace the text "as though you entered a <Return> to the boot
prompt" with "as though you typed the default boot string, adding the
keyword auto". Note that when autobooting, the system will proceed directly
to multi-user mode, rather than entering system maintenance mode first.

Trusted Facility Manual

Pages 123-125: The event type names given in the text do not precisely
match those shown on the screen. Replace "Startup/Shutdown" with
"Startup/Shutdown activity". Replace "User Login/Logout" with "Login/Logoff
Activity". Replace "Process Start/Stop" with "Process creation/deletion
activity". Replace "Object Allocation" with "Make object available".
Replace "Object Mapping" with "Map object to subject". Replace "Object
Modification" with "Modify object". Replace "Object Deallocation" with
"Make object unavailable". Replace "DAC Modification" with "Discretionary
access change". Replace "Admin Actions" with "System administrator
activity". Replace "IPC Communication" with "Inter-process communication".
Replace "Process Modification" with "Modify process". Replace "Audit
Changes" with "Audit subsystem activity". Replace "Subsystem Changes" with
"Privileged subsystem activity". Replace "Privilege Use" with "Use of
privilege". Replace "Authorization Use" with "Use of authorization".
Replace "Label Changes" with "Set policy label". Replace "X Window Events"
with "Window system activity".

Page 124: In the paragraph previously headed "Admin Actions", replace
the text "or Operator" with "Network Security Officer or Operator".

Page 125: Add to the paragraph previously headed "Label Changes": "This
event type also includes changes to access control lists, clearances and
information labels."

Trusted Facility Administrator's Reference Manual

Page 113 auth: Note that the auth command authorisation implies the
password command authorisation.

Page 119 lp: Note that the lp command authorisation implies the printerstat
command authorisation.

MaxSix Administrator's Guide

Page 32: Disregard the text "except the indirect flag" - this flag is not
present in this release.

Page 133: Disregard the -v option on the ping command.

Appendix A. Security Features User's Guide - Errata

Page 7: Note that the administrator may have set a minimum password change
time on your account, which could prevent you from completing the password
change successfully. If this occurs, you will need to contact your system
administrator to have the minimum password change time reset.

Page 11: Note that the administrator may have set an inactivity timeout for
your system. If this is the case, your user session will be automatically
locked or terminated if you leave your session idle (i.e. without keyboard
or mouse input) for the administrator-specified time. The inactivity
timeout is not initiated until the login sequence has completed, when the
security stripe will be shown at the bottom of the screen.

Page 67: After the text "To set a file's set-group-ID bit when the file is
group executable," add "you must have the chmodsugid base privilege and".

Page 83: At the end of the mandatory write access paragraph, add "In
addition, with the default privilege set (which includes the writeup
privilege), a process can write to a file if the process's sensitivity
label is dominated by the object's."

Page 83 diagram: The text in the grey oval should read "Confidential".

Page 88 table: The first item in the Relationship column should read "A
Dominates B".

Page 109: The grey ovals should be filled with the following text - from
left to right: "Confidential Nato", "Secret", "Secret Alpha".

Page 115 step 1: Add the text "then select Get/Set File Label from the
File Operation options menu".

Page 115 step 4: Replace the text "the following figure" with "the previous
figure".

Page 163: Disregard the paragraph labelled syshi - this authorisation is
not present in this release.